## Slide 1
ROUND 1 · PROPOSAL PRESENTATION
Safe Road-Crossing
Assistance System
A computer-vision system that watches a road crossing and gives spoken guidance on when it is safe to cross — for visually impaired and elderly pedestrians.
Governing design rule: default output is always WAIT. Only explicit positive evidence produces “safe to cross.”
[Team Member Name 1] · [Team Member Name 2] · [Team Member Name 3]
Guide: [Guide Name] [Presentation Date]

## Slide 2
ROUND 1 AGENDA
Six sections, one governing idea
01
Introduction
The problem, the user, and the one rule everything else follows from
02
Literature Review
What existing work covers — and what it assumes away
03
Research Gap
Pieces exist; an integrated, safety-asymmetric decision layer doesn't
04
Methodology
Detection, tracking, monocular TTC, and a 6-rule decision layer
05
System Architecture
How the pipeline is wired, end to end
06
Workflow
The six sequential rules, and why WAIT is the default path
Introduction
1 / 17
Notes: This is the map for Round 1. All six sections are proposal-stage: design and justification, not results. Emphasize up front that end-to-end validation is ongoing — this talk is about why the system is built this way, not a claim that it works. Likely question: "why isn't there a results section?" Answer: this round is scoped to design; Round [X] covers evaluation once ground-truth annotation is complete.

## Slide 3
INTRODUCTION
The problem
Visually impaired and elderly pedestrians rely on audible or tactile cues that many crossings simply don't provide.
Existing assistive tools (white cane, guide dog, hearing) detect obstacles at arm's length — not an approaching vehicle 40 metres away.
A wrong “safe” costs a life. A wrong “wait” costs a few seconds.
What we're building
A camera at the kerb watches a signalised crossing. Vision pipeline detects vehicles, pedestrians, crosswalks and signals. Spoken guidance tells the user when it is genuinely safe to cross. Runs on a PC, CPU inference — no phone, no embedded hardware.
Introduction
2 / 17
Notes: Frame this as an assistive aid, not a replacement for a white cane or the user's own judgement — say that explicitly if asked. Likely question: "why a fixed camera and not a wearable?" Answer: proposal scope is a fixed-installation assistive system at a known crossing; a wearable form factor is future work, not what's being evaluated here.

## Slide 4
INTRODUCTION
The governing design rule
Every decision in this system — thresholds, hysteresis, confidence gates, even how frame-skipping is implemented — follows from one asymmetry.
FALSE “WAIT”
Merely inconvenient
The system tells the user to wait when the road was actually clear. The user waits a few extra seconds. Nothing worse happens.
FALSE “SAFE”
The only unacceptable failure mode
The system tells the user to cross when a vehicle is actually approaching. This can kill someone. It is the one outcome the entire design optimises against.
Introduction
3 / 17
Notes: This slide is the thesis statement of the whole project — refer back to it in every later section ("this is why confidence gating is asymmetric", "this is why hysteresis is asymmetric"). Likely question: "isn't excessive WAIT its own safety problem, since users stop trusting the system?" Answer: yes — that's exactly why UNKNOWN vehicle states and the crossing-time margin exist, so caution doesn't collapse into permanent, useless WAIT (see Methodology).

## Slide 5
LITERATURE REVIEW
What the pieces look like in prior work
Area
Key work
Relevance to us
Object detection
YOLO family (YOLOv1–v8, Redmon et al.; Ultralytics)
Real-time single-shot detection — the backbone of our detector
Multi-object tracking
ByteTrack (Zhang et al., 2022)
Associates detections across frames using low-confidence boxes too, not just high-confidence ones
Benchmarks
COCO (Lin et al., 2014), Cityscapes (Cordts et al., 2016)
Standard detection/segmentation benchmarks; general-scene, not crossing-specific
Indian road datasets
IDD (Varma et al., 2019)
Driver-viewpoint Indian road scenes; dashcam angle, not pedestrian-kerb angle
Monocular TTC
Classical time-to-contact / optical-expansion literature (Lee, 1976 and successors)
[CITATION NEEDED — verify before submission]
Pedestrian-signal / crossing assistance
[CITATION NEEDED — verify before submission]
Assistive crossing-detection systems for visually impaired users
Literature Review
4 / 17
Notes: IMPORTANT FOR THE STUDENT: rows marked [CITATION NEEDED] must be filled with real, verified references before submission — do not present them to examiners as-is. I did not fabricate authors/years/DOIs for the TTC and assistive-crossing rows because I'm not confident enough in specific paper identities to state them as fact; verify Lee's 1976 tau-function paper and find real assistive-pedestrian-crossing CV papers (search terms: 'pedestrian traffic signal recognition blind', 'crosswalk detection assistive vision'). Likely question: "what specifically does ByteTrack do differently from SORT?" Answer: it keeps low-confidence detection boxes in the association step instead of discarding them, which recovers tracks during occlusion — useful here because a partially-occluded approaching vehicle is exactly the dangerous case.

## Slide 6
LITERATURE REVIEW
What the literature assumes away
!
Symmetric metrics
mAP treats a missed red light and a missed green light as equally costly. For this application they are not remotely equal.
!
Calibrated depth
Monocular TTC / depth work generally assumes a calibrated camera or known object dimensions. A kerb-mounted camera at an arbitrary crossing has neither.
!
Confident evidence only
Little published work addresses what a system should do when evidence is absent or ambiguous — the common case in practice, and the case where a wrong answer is lethal.
Literature Review
5 / 17
Notes: This slide sets up Research Gap directly — each of these three bullets becomes one gap on the next section. Likely question: "can you name a specific paper that uses a symmetric metric here?" Answer: point to mAP itself as the standard detection metric (used by essentially all YOLO/Ultralytics benchmarking, including our own training runs) — it is class-symmetric by construction, weighting every class's AP equally regardless of the real-world cost of an error in that class.

## Slide 7
RESEARCH GAP
The pieces exist. The integration doesn't.
Pedestrian detection, traffic-light recognition, crosswalk segmentation, and monocular depth/TTC are each independently studied. The gap is an integrated, safety-asymmetric decision system built on top of them.
Pedestrian
detection
Traffic-light
recognition
Crosswalk
segmentation
Monocular
depth / TTC
+
+
+
↓
Missing: an integrated, safety-asymmetric decision layer
What should the system do when evidence is absent, ambiguous, or contradictory — and treat a false SAFE as categorically worse than a false WAIT?
Research Gap
6 / 17
Notes: Likely question: "isn't a decision tree over detector outputs pretty simple — where's the research contribution?" Answer: the contribution isn't the branching logic's complexity, it's the derivation of every threshold and asymmetry from an explicit safety criterion (confidence gating, hysteresis asymmetry, the TTC noise horizon) rather than hand-tuned constants — that derivation is what Methodology covers next.

## Slide 8
RESEARCH GAP
A gap we found ourselves
A class can score 0.93 mAP50 on a validation split and still detect almost nothing on real street footage from a different setting.
Validation-split metrics conceal domain gaps — and for a safety system, the split metric is not the metric that matters.
Observed directly in this project:
crosswalk class
0.932
mAP50 on the held-out validation split
vs. 1 detection at 0.28 confidence on a real Creative-Commons street clip (preliminary, single clip)
Downstream effect
crosswalk is Decision Rule 1. When it silently fails on real footage, no later rule is ever evaluated — the system sits in SEARCHING regardless of what else is true.
Research Gap
7 / 17
Notes: Be precise if questioned: this is one preliminary observation from one real-world clip, not a measured domain-gap rate — do not let it be quoted back as a validated statistic. Likely question: "so does the system just fail in practice?" Answer: this is exactly why Round 1 is proposal-stage — it's the motivating evidence for why validation methodology (Round [X]) must test on real, out-of-distribution footage rather than trust the validation-split number alone.

## Slide 9
METHODOLOGY
Detection & tracking
YOLOv8 + ByteTrack — 10 classes, trained AND run at 960px
car · bus · truck · motorcycle · autorickshaw · person · crosswalk · signal_red · signal_green · signal_countdown
Overall mAP50
0.829
Why 960px, not the 640px default:
A pedestrian signal head is often only 20–30px wide in a 1080p frame. At the 640px default that resolution is destroyed by downscaling before the detector ever sees it — signals appeared to fail completely at 640px, and did not; it was a resolution mismatch between training and inference, not a model failure.
Why ByteTrack:
Persistent per-vehicle track IDs are the input the TTC estimator needs — a box-growth fit is only meaningful across frames of the same physical vehicle, not a fresh detection each frame.
Methodology
8 / 17
Notes: Likely question: "why not a smaller/faster model given CPU-only inference?" Answer: the resolution requirement (960px, driven by signal-head size) dominates the speed budget more than model size does — see the frame-skipping slide for how the fps floor is actually met. Likely question: "is 0.829 good?" Answer: don't claim so in isolation — the per-class table (next-but-one slide) is the honest picture, since it's an average over classes with very different amounts of training data.

## Slide 10
METHODOLOGY
Per-class detection accuracy (mAP50)
Chart: 
| car | crosswalk | autorickshaw | motorcycle | truck | person | bus | signal_red | signal_green
mAP50 | 0.939 | 0.932 | 0.921 | 0.877 | 0.839 | 0.765 | 0.738 | 0.731 | 0.721
Trained and inferred at 960px, single held-out validation split. signal_countdown not shown — no labelled examples exist yet (see next slide).
Methodology
9 / 17
Notes: Likely question: "why is signal_green/signal_red the weakest pair?" Answer: they had zero training data from public datasets (checked against the actual data.yaml of every source dataset) and were entirely bootstrapped from three small CC traffic-light datasets added later in the project — they're the newest classes, not a flaw in the approach. Likely question: "why exclude signal_countdown from this chart entirely rather than showing 0.0?" Answer: 0.0 mAP50 would misleadingly read as 'the model tried and failed' — the honest fact is no public dataset has boxed countdown annotations, so the class has never been trained; that's a data-collection gap, addressed next.

## Slide 11
METHODOLOGY
Time-to-contact: the reciprocal-width fix
Monocular TTC, estimated from bounding-box growth — no calibrated camera, no known object dimensions.
The naive approach
Fit box width w linearly over time.
But w = k / D (distance) — hyperbolic, not linear. A linear fit systematically underestimates the current closing rate.
Result: TTC over-reported by ~0.3–0.35s — optimistic, worsening as the vehicle gets closer. The one direction this system must never err in.
Our fix
Fit u = 1/w linearly over time instead.
Since u ∝ D, u is exactly linear under constant velocity — not an approximation to the curve, the correct model.
Result: error reduced to under 0.005s on synthetic ground truth.
TTC = u / (−du/dt), verified against synthetic constant-velocity sequences (real footage is too sparse in vehicle detections to serve as ground truth yet).
Methodology
10 / 17
Notes: Likely question: "what if the vehicle accelerates rather than moving at constant velocity?" Answer: an accelerating vehicle is still estimated optimistically under this constant-velocity model — this is a known, documented limitation, and it's exactly why the decision layer keeps its own 3-second crossing-time margin on top of TTC rather than trusting the number as exact (see Decision Logic). Likely question: "why synthetic data and not real footage for this number?" Answer: honest answer — the available real clips barely produce sustained vehicle tracks, so 'it looked right on video' would prove nothing; synthetic constant-velocity sequences give exact ground truth to measure error against.

## Slide 12
METHODOLOGY
Three-state track assessment
Box jitter alone can look like motion. A fixed threshold on apparent approach rate is wrong at every scale — too strict for distant boxes, too loose for close ones.
APPROACHING
Fit succeeds; closing rate exceeds the noise floor. Real evidence of danger.
NOT_APPROACHING
Fit succeeds; TTC is beyond the noise horizon AND that horizon comfortably clears the 5s decision threshold. Real evidence of safety.
UNKNOWN
Too few samples, a degenerate fit, or a box too small to trust either way. Evidence of nothing — in either direction.
Why UNKNOWN matters: an early design where any unassessed vehicle blocked SAFE meant a single parked car blocked SAFE forever. And a vehicle turning laterally across the crossing is reported UNKNOWN, not NOT_APPROACHING — because lateral motion alone would otherwise dismiss a genuine turning-vehicle hazard.
Methodology
11 / 17
Notes: This is a viva favorite — be ready to trace the exact failure mode by hand. Likely question: "walk me through why a turning vehicle would be misread without this fix." Answer: a vehicle turning across the crossing moves mostly sideways, so its box grows slowly — weak box growth alone looks identical to a distant/parked vehicle and would satisfy the 'beyond noise horizon' condition for NOT_APPROACHING, which fsm.py treats as safety evidence. The fix checks a lateral crossing_ratio first and forces UNKNOWN when it's set, before the growth-based classification ever runs.

## Slide 13
METHODOLOGY
Confidence asymmetry & hysteresis
Evidence for danger is cheap to accept. Evidence for safety is expensive.
Confidence gate
signal_red: trusted at ANY confidence. crosswalk, signal_green: trusted only above 0.6 confidence — these are the only classes that can push toward SAFE.
Asymmetric hysteresis
Entering SAFE: requires 8 consecutive agreeing frames. Leaving SAFE: immediate, on the very next frame.
Slow to permit. Instant to withdraw.
Methodology
12 / 17
Notes: Likely question: "why 0.6 and 8 frames specifically, not some other number?" Answer: be honest — these are engineering choices consistent with the safety asymmetry, not derived from a measured false-positive rate (unlike the TTC noise horizon, which IS derived). Flag this if asked: validating and possibly re-tuning these two constants against real false-accept/false-reject rates is exactly what the ground-truth evaluation phase (mentioned in Workflow's last slide) is for.

## Slide 14
METHODOLOGY
Frame skipping without faking evidence
Detector runs every Nth frame (default N=2) to hit the fps target on CPU.
Chart: 
| detect-every 1 | detect-every 2 | detect-every 3
fps | 9.4 | 16.5 | 21.6
Measured on a 1920×1080 clip, headless, imgsz 960.
What does NOT run on skipped frames — and why
Tracker & decision logic do not re-run on a carried-forward detection. Re-feeding an identical box at a later timestamp would inject fake zero-growth into the TTC fit — making an approaching vehicle look slower than it is.
That's optimistic. The one direction this system must never take.
Methodology
13 / 17
Notes: Likely question: "doesn't skipping frames mean you might miss a hazard that appears and disappears within the skip?" Answer: yes, and that's a stated residual risk, not eliminated — a hazard first appearing on a skipped frame is unevaluated for up to N-1 frames. N=2 (the default) is the conservative choice for exactly this reason, not N=3 which was also measured and is faster.

## Slide 15
SYSTEM ARCHITECTURE
End-to-end pipeline
Camera
feed
→
Detector
(YOLOv8, 960px)
→
Tracker
(ByteTrack)
→
TTC
Estimator
→
Decision
Rules
→
Hysteresis
→
Audio
Output
SQLite decision log
(per-frame)
Frame skipping runs the detector every Nth frame only; the tracker, TTC estimator and decision rules process every detector output that exists — never a carried-forward duplicate.
System Architecture
14 / 17
Notes: Likely question: "where exactly does frame-skipping sit in this diagram?" Answer: it gates entry to the Detector box — on a skipped video frame, the Detector box doesn't run at all and every stage after it (Tracker onward) simply reuses the last real output, per the previous slide. Likely question: "why log every frame, including skipped ones?" Answer: so evaluate.py's fps calculation counts real video frame rate, not just detection rate — logged separately with an is_detection_frame flag.

## Slide 16
WORKFLOW
Six sequential rules — plain Python, no state machine
Every branch must be explainable in a viva. Rules are checked in order; the first match wins.
1
No crosswalk detected
SEARCHING
Nothing else is evaluated without a known legal crossing point
2
signal_red present
WAITING
Unconditional — checked before anything that could emit SAFE
3
A vehicle is turning across the crossing
WAITING
TTC cannot see a turning vehicle's real risk at all
4
A vehicle's TTC < 5.0s
WAITING
An imminent, head-on hazard
5
signal_green AND road honestly assessable as clear
SAFE
The only rule that can emit SAFE — both conditions required
6
Otherwise
WAITING
The default. Reached whenever evidence is absent or ambiguous
Workflow
15 / 17
Notes: Likely question: "why plain if/elif instead of a state-machine library?" Answer: PLAN.md's own ground rule — every branch must be individually explainable in a viva; a library state machine adds indirection with no behavioral benefit at this scale (three real output states: SEARCHING, WAITING, SAFE_TO_CROSS). Likely question: "why is 'vehicle turning' checked before the TTC rule rather than folded into it?" Answer: TTC models head-on closing distance and literally cannot represent a turning vehicle's risk — folding it into the TTC check would silently misrepresent what's being measured, so it's a structurally separate rule with its own veto.

## Slide 17
WORKFLOW
Default is WAIT — the path visualised
SAFE has exactly one door in. Every other path — including every failure, exception, and low-confidence frame — leads to WAITING.
No crosswalk?
↓ no
signal_red present?
↓ no
Vehicle turning?
↓ no
TTC < 5.0s?
↓ no
signal_green + road clear?
WAITING
The default. Reached by four of the five checks shown, every exception, and every low-confidence read.
SAFE_TO_CROSS — reached only when BOTH conditions hold
Workflow
16 / 17
Notes: This is the single most important slide to get right visually — the point is that WAIT is the fat basin and SAFE is one narrow gate at the very bottom. Likely question: "what happens on a caught exception mid-pipeline?" Answer: the whole update() call is wrapped so any exception anywhere in decision-making returns WAITING — deliberately bare, because there's no failure mode this system is willing to let fall through to SAFE by default.

## Slide 18
Where this stands, honestly
BUILT
Detector + tracker + monocular TTC + 6-rule decision layer + threaded audio + per-frame SQLite logging
NOT YET CLAIMED
No false-safe rate, no overall accuracy figure, no proof on real footage — end-to-end validation is ongoing
NEXT ROUND
Ground-truth annotation, ByteTrack-linked TTC error on real tracks, and the false-safe rate measured honestly
Questions?
Closing
17 / 17
Notes: Close on this slide deliberately — it pre-empts the most likely panel question ("where are your results?") by stating plainly that this round is proposal-stage and naming the specific next steps rather than dodging the question.