## Slide 1
FINAL-YEAR ENGINEERING PROJECT · REVIEW ROUND 1
Safe Road-Crossing
Assistance System
A computer-vision system that watches a road crossing through a camera and tells a visually impaired or elderly pedestrian, out loud, when it is safe to cross.
WAIT
is the default. SAFE is said only on explicit positive evidence.
Parth Agrawal · Atul Bharathi · Sarvesh Pande · Kishan Shakya · Abhishek Dixit
Guide: [Guide name] · [Department, College] · 2026
WAIT
default
SAFE
earned
Notes: Round 1 covers the problem, prior work, the research gap, the method, the architecture and the workflow. Results and evaluation come in later rounds. Replace the bracketed placeholders with the guide name and department.

## Slide 2
INTRODUCTION
Crossing a road is a judgement made with the eyes
Judging gaps in traffic and reading signals is hard without good sight. This system watches the crossing for you and says what it sees.
Safe Road-Crossing Assistance System · Review Round 1
2
approaching
signal
camera + PC
“Wait. Vehicle approaching.”
Who it helps
Visually impaired and elderly pedestrians at a road crossing.
What it sees
One fixed camera watching the crossing, the traffic and the signal.
What it says
Short spoken guidance, plus distinct tones that need no words.
Where it runs
A standard PC with CPU inference. No special hardware.
Notes: Top view of a crossing. The camera sees the crosswalk, the signal and the traffic. The PC runs the vision pipeline and the pedestrian hears a spoken verdict.

## Slide 3
INTRODUCTION
The core idea: the two possible mistakes are not equal
Every decision has two ways to be wrong. The design is built around the fact that one of them is catastrophic.
Safe Road-Crossing Assistance System · Review Round 1
3
Road is actually
SAFE
Road is actually
DANGEROUS
System says WAIT
System says SAFE
False WAIT
An inconvenience. The pedestrian waits a little longer.
Correct
The pedestrian is protected.
Correct
The pedestrian crosses on time.
False SAFE
Can kill someone. The only unacceptable error.
So the design rule is:
WAIT is the default.
SAFE must be earned with explicit positive evidence.
Danger evidence is accepted cheaply
A red light is trusted at any confidence
Safety evidence must be strong
Green light and crosswalk need confidence ≥ 0.6
Withdrawing SAFE is instant
Entering SAFE needs 8 agreeing frames
Notes: This 2x2 is the intellectual core of the project. Every later design choice (confidence gating, hysteresis, unknown-means-wait) is a consequence of the bottom-right cell.

## Slide 4
LITERATURE REVIEW
Each building block already exists in the literature
Four research threads supply the parts. This project assembles them and adds the safety logic.
Safe Road-Crossing Assistance System · Review Round 1
4
Object detection
Two-stage: R-CNN, Faster R-CNN
Girshick et al., CVPR 2014 · Ren et al., NeurIPS 2015
Single-stage: YOLO
Redmon et al., CVPR 2016
Single-stage: SSD
Liu et al., ECCV 2016
Used here: YOLOv8 (Ultralytics, 2023)
Multi-object tracking
SORT
Bewley et al., ICIP 2016
DeepSORT
Wojke et al., ICIP 2017
ByteTrack
Zhang et al., ECCV 2022
Used here: ByteTrack
Time-to-contact & depth
Time-to-contact from image expansion (τ)
Lee, Perception, 1976
Depth from a single image
Eigen et al., NeurIPS 2014
Used here: the τ idea, calibration-free
Assistive crossing aids
Signal & crosswalk recognition for blind pedestrians
[CITATION NEEDED — verify before submission]
Phone / wearable camera crossing aids
[CITATION NEEDED — verify before submission]
Motivates: the user need
DATASETS & BENCHMARKS
PASCAL VOC — Everingham et al., IJCV 2010
COCO — Lin et al., ECCV 2014
Cityscapes — Cordts et al., CVPR 2016
Notes: All citations on this slide are well-known works; two slots are deliberately marked CITATION NEEDED because assistive-crossing papers must be chosen and verified by the team. Check every venue and year against the actual paper before submission.

## Slide 5
LITERATURE REVIEW
From region proposals to one-pass detection and tracking
Safe Road-Crossing Assistance System · Review Round 1
5
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
DETECTION
TRACKING
R-CNN
Girshick et al., CVPR
Faster R-CNN
Ren et al., NeurIPS
YOLO
Redmon et al., CVPR
YOLOv8
Ultralytics (software)
USED HERE
successive single-stage releases, 2017–2022
SORT
Bewley et al., ICIP
DeepSORT
Wojke et al., ICIP
ByteTrack
Zhang et al., ECCV
USED HERE
two-stage: propose regions, then classify
single-pass detection / tracking
The trend: fewer stages, one forward pass, real-time on ordinary hardware. Those are the properties a live safety aid needs.
Notes: Detection moved from two-stage (R-CNN, Faster R-CNN) to single-pass (YOLO) designs. Tracking moved from SORT to DeepSORT to ByteTrack, which also uses low-confidence boxes during association.

## Slide 6
RESEARCH GAP
The gap: the parts exist, safety-aware integration does not
Safe Road-Crossing Assistance System · Review Round 1
6
GAP 1
Standard metrics are symmetric
mAP scores a missed red light and a missed green light as the same error. For a pedestrian they are not remotely equivalent.
GAP 2
Monocular TTC assumes calibration
Typical methods need a calibrated camera or known object sizes. A deployable assistive system should need neither.
GAP 3
Absent or ambiguous evidence is ignored
Little work says what to do when nothing clear is seen. That is the common real-world case, and the dangerous one.
mAP penalty
Real consequence
missed red
missed green
walks into traffic
waits longer
=
≠
camera calibration
known vehicle size
stereo or depth sensor
Needed here: box width over time
most real frames
ambiguous / nothing seen
danger
safe
this project: → WAIT
This project: one integrated pipeline in which every uncertain case resolves to WAIT.
Notes: Gap 1: detection metrics are symmetric. Gap 2: monocular TTC usually needs calibration or known sizes. Gap 3: behaviour under absent or ambiguous evidence is rarely specified. The contribution is the integration plus explicit asymmetry.

## Slide 7
METHODOLOGY
Detection: YOLOv8 finds every object in one pass
Safe Road-Crossing Assistance System · Review Round 1
7
TWO-STAGE (e.g. Faster R-CNN)
car?
bus?
background?
image
propose many regions
classify each region
detections
SINGLE-STAGE (YOLO)
One network pass: a grid predicts boxes, classes and confidences together
image
detections
Why single-stage for a safety aid
Latency is safety
A late answer about a moving car is a wrong answer.
Runs on a CPU
Interactive frame rates on a standard PC.
One model, ten classes
Vehicles, people, crosswalks and signals in a single pass.
10 CLASSES
car
bus
truck
motorcycle
autorickshaw
person
crosswalk
signal_green
signal_red
signal_countdown
grey context green evidence toward SAFE (confidence-gated) red evidence toward WAIT amber no training data yet, not used in decisions
Notes: Two-stage detectors first propose candidate regions, then classify each one. YOLO predicts boxes and classes for the whole image in a single network pass, which is what makes CPU real-time feasible.

## Slide 8
METHODOLOGY
Detector accuracy per class: a component metric
Safe Road-Crossing Assistance System · Review Round 1
8
0.829
overall mAP50
Mean Average Precision at box overlap (IoU) ≥ 0.5, on the detector’s validation set.
Component metric only
This measures how well the detector finds and labels objects. It is not a measure of whole-system accuracy or safety.
Chart: 
| signal_green | signal_red | bus | person | truck | motorcycle | autorickshaw | crosswalk | car
large / near objects | 0 | 0 | 0.738 | 0.765 | 0.839 | 0.877 | 0.921 | 0.932 | 0.939
signal heads | 0.721 | 0.731 | 0 | 0 | 0 | 0 | 0 | 0 | 0
large / nearby objects
traffic-signal heads
Why signals score lower
car
signal
A distant signal head may be only a few pixels wide. A nearby car fills a large part of the frame. Small objects are inherently harder to detect.
signal_countdown is not scored: no labelled data yet.
Notes: Per-class mAP50 from the trained detector. Sorted high to low. The two signal classes are highlighted because they are small, distant objects. This is the accuracy of one component, not of the whole crossing system.

## Slide 9
METHODOLOGY
Tracking: ByteTrack gives every vehicle a stable identity
One frame shows where things are. Only identity across frames shows which way they are moving.
Safe Road-Crossing Assistance System · Review Round 1
9
Detection only
?
dashed = frame t solid = frame t+1
Which box is which? Growth and shrinkage cannot be measured.
Detection + tracking
#7
#3
#7 growing:
approaching
#3 shrinking:
receding
dashed = frame t solid = frame t+1
Same ID across frames, so each box’s change in size is measurable.
1
Predict
A motion model predicts where each existing track moves next.
2
Match strong boxes
High-confidence detections are matched to predictions by box overlap (IoU).
3
Rescue weak boxes
Leftover low-confidence boxes get a second match, so IDs survive partial occlusion.
4
Keep history
Each ID stores its recent box widths. This is the input to TTC.
Notes: Without identity you cannot tell approach from recession. ByteTrack predicts track motion, matches high-confidence boxes by IoU, then runs a second association with low-confidence boxes so tracks survive occlusion.

## Slide 10
METHODOLOGY
As a vehicle approaches, its box grows: w = k / D
A bounding box is the only distance cue a single uncalibrated camera gives us.
Safe Road-Crossing Assistance System · Review Round 1
10
D = 40 m w = 30 px
D = 20 m w = 60 px
D = 10 m w = 120 px
approaching
w = k / D
w box width in pixels
D distance to the vehicle
k focal length × real width: unknown, and never needed
Halve the distance → double the width
40 m
30 px
20 m
60 px
10 m
120 px
Notes: Pinhole geometry: apparent width is inversely proportional to distance. The constant k combines focal length and the true vehicle width. We never need to know it, because it cancels in the TTC calculation on the next slide.

## Slide 11
METHODOLOGY
Time-to-contact without calibration: straighten the curve
Safe Road-Crossing Assistance System · Review Round 1
11
Width w vs time: a curve
w = k / D is a hyperbola in time, so a straight-line fit on w is biased.
w
time →
contact
true w shoots up
near contact
straight fit on w:
far too slow
measured samples
u = 1/w vs time: a straight line
u = D / k falls linearly at constant speed. Extrapolate it to zero.
u
now
contact: u = 0
extrapolate
TTC
time →
w = k / D
u = 1/w = D / k
constant speed ⇒ D, and so u, fall linearly
fit a line to recent u; TTC = u / (−du/dt)
k cancels: no calibration
Notes: Width against time is a hyperbola, so a linear fit on w underestimates growth and overestimates the time left. Its reciprocal u = 1/w = D/k is exactly linear in time at constant closing speed. Fit a line to the last few u samples and extrapolate to u = 0: TTC = u / (−du/dt). The unknown constant k cancels, so no camera calibration or vehicle size is needed.

## Slide 12
METHODOLOGY
Measurement limit: box jitter looks like motion
Even on a parked car, a detector’s box edges wobble by a pixel or two from frame to frame (assumed δ ≈ 1.5 px).
Safe Road-Crossing Assistance System · Review Round 1
12
Same jitter, very different meaning
distant box
w ≈ 20 px
jitter = 7.5 % of w
near box · w ≈ 200 px
jitter = 0.75 % of w
Fake “approach” from jitter shrinks fast with size
noise rate ≈ δ / (w² · T)
box width w →
any single fixed threshold
too loose here:
jitter passes as motion
too strict here: slow real
approaches hide below it
So the limit scales with the box
TTC_horizon = w·T / δ
beyond it, a TTC is indistinguishable from jitter
APPROACHING
TTC inside the horizon: real motion, trusted
NOT APPROACHING
beyond the horizon, and horizon ≥ 2 × 5 s
UNKNOWN → blocks SAFE
horizon too short to tell: never read as safe
Notes: A ±1.5 px wobble is 7.5% of a 20 px box but 0.75% of a 200 px box. The apparent approach rate that noise alone can fake scales as δ/(w²T), so no single fixed threshold works across sizes. Instead the system converts this into a TTC noise horizon that grows with box size, and returns UNKNOWN (which blocks SAFE) when the horizon is too short to trust.

## Slide 13
METHODOLOGY
Evidence of danger is cheap; evidence of safety must be strong
The same detector confidence is treated differently depending on which way the evidence pushes.
Safe Road-Crossing Assistance System · Review Round 1
13
0.0
0.2
0.4
0.6
0.8
1.0
detector confidence →
signal_red
danger evidence
below detector floor
ACCEPTED at any confidence → WAIT
signal_green
safety evidence
below detector floor
ignored → treated as absent
ACCEPTED
crosswalk
safety evidence
below detector floor
ignored → treated as absent
ACCEPTED
detector floor 0.40
safety gate 0.60
Red light seen at 0.45 → trusted → WAIT
Green light seen at 0.45 → ignored, falls through → WAIT
Notes: A false-positive red only causes extra caution, so red is trusted at whatever confidence the detector reports. Crosswalk and green both push toward SAFE, so they must clear 0.6. Between 0.4 and 0.6 they are treated as not seen, which falls through to WAIT (or SEARCHING for a crosswalk). Uncertainty can only ever push toward WAIT.

## Slide 14
SYSTEM ARCHITECTURE
End-to-end pipeline: one frame’s path from camera to voice
Safe Road-Crossing Assistance System · Review Round 1
14
PERCEPTION
MEASUREMENT
SAFETY LOGIC
OUTPUT
Camera
live video
frames
YOLOv8
detector · 10 classes
boxes · class · conf
ByteTrack
tracker · stable IDs
IDs · width history
TTC
1/w regression · noise horizon
TTC + status per vehicle
Rules
6 ordered rules
raw verdict + reason
Hysteresis
8 frames in, instant out
stable state
Audio
speech + earcons
spoken guidance
runs only on every Nth frame (detect → track → estimate → decide → vote)
Decision log · SQLite
every frame’s state, reason and inputs, for offline evaluation
One standard PC · CPU inference · no camera calibration · no special hardware
Notes: The anchor diagram. Perception (camera, detector, tracker) feeds measurement (TTC), which feeds the safety logic (six rules, then asymmetric hysteresis), which drives audio. Every decision is also written to a SQLite log by a background thread.

## Slide 15
SYSTEM ARCHITECTURE
Speed-up: detect every Nth frame, and never fake the gaps
Safe Road-Crossing Assistance System · Review Round 1
15
1
2
3
4
5
6
7
8
9
10
11
12
Camera frame
YOLOv8 + ByteTrack
TTC + rules + vote
Announced state
skip
skip
skip
skip
skip
skip
skip
skip
skip
skip
skip
skip
holds the last real verdict between detections
N = 2: the detector runs on every 2nd frame, roughly doubling throughput. Skipped frames produce no new measurement, and the 8-frame vote counts real looks only.
Correct: fit only real measurements
w
time →
Only frames the detector actually saw enter the width history, each with its true timestamp.
Wrong: reuse the old box with a new timestamp
w
time →
Stale widths (hollow) sit below the truth. The vehicle looks farther and slower than it is, so TTC comes out too long: a bias toward a false SAFE.
Notes: Running the detector on every Nth frame roughly doubles throughput at N=2. Tracking, TTC, rules and the hysteresis vote run only on frames that were actually detected. If a skipped frame reused the previous box with a new timestamp, widths would lag the truth, the fitted approach would look slower, and TTC would be overestimated: the dangerous direction.

## Slide 16
SYSTEM ARCHITECTURE
Output: speech never blocks vision, and every decision is logged
Safe Road-Crossing Assistance System · Review Round 1
16
Speech thread
text-to-speech + earcons
Vision thread
main loop, never waits
Logger thread
batched database writes
capture frame
detect + track
TTC + rules + vote
next frame, no waiting
queue
queue
rate limit
speak + tone
batch: 50 rows / 0.5 s
decisions.db
hand-off is non-blocking: vision never waits for speech or disk
every frame’s state, reason and inputs, for offline evaluation
Earcons: meaning before words
SAFE
rising two-tone, C5 → G5
WAIT
three low pulses, 220 Hz
Rate-limited to avoid chatter, except warnings
“safe to cross”
plays
same message
within 2 s: dropped
2 s cooldown
new WAIT warning: always plays, jumps the queue
Notes: Speech and logging each run in their own thread behind a queue, so the vision loop never blocks. Earcons give instant, language-free meaning. Repeated messages are rate-limited, but a transition into WAIT bypasses every limit and drops stale pending speech.

## Slide 17
WORKFLOW
Every frame: six rules, checked in order, and most exits say WAIT
Safe Road-Crossing Assistance System · Review Round 1
17
each
frame
RULE 1
conf ≥ 0.6
Crosswalk seen?
RULE 2
any conf
Red signal?
RULE 3
Vehicle turning across?
RULE 4
Any TTC < 5 s?
RULE 5
conf ≥ 0.6
Green AND road clear?
yes
no
no
no
yes
SAFE
the only way in,
then an 8-frame vote
no
SEARCHING
yes
yes
yes
no (rule 6)
WAIT the default: 4 of the 6 outcomes land here
Rule 6: anything not explicitly safe (no signal seen, a low-confidence green, a vehicle not yet assessable) falls through to WAIT.
Notes: Rules are checked in order and the first match wins. Rule 1 gates everything on a confident crosswalk. Rules 2, 3 and 4 are danger checks that force WAIT. Rule 5 is the only rule that can produce SAFE, and it needs a confident green AND a road that is assessably clear: no unresolved vehicle, and any approaching vehicle’s TTC longer than the time needed to walk the crossing. Rule 6 is the default.

## Slide 18
WORKFLOW
Hysteresis: slow to permit, instant to withdraw
Safe Road-Crossing Assistance System · Review Round 1
18
frame
Raw rule verdict
(this frame only)
Agreement counter
Announced state
1
W
2
W
3
S
1
4
S
2
5
W
↺
6
S
1
7
S
2
8
S
3
9
S
4
10
S
5
11
S
6
12
S
7
13
S
8
14
S
15
S
16
W
17
W
18
S
1
19
S
2
20
S
3
WAIT
SAFE
WAIT
one flicker resets
the count
8 consecutive agreeing frames before SAFE is announced
one disagreeing frame:
WAIT on the very same frame
Entering SAFE: an 8-frame vote
A single flickered green detection must never tell someone to step into the road.
Leaving SAFE: immediate, no vote
The one state where being slow to change is dangerous is the one being left.
Notes: Top row: what the rules say on each frame. Middle: the vote counter. Bottom: what is actually announced. A single WAIT in the run at frame 5 resets the count. SAFE is announced only at frame 13, after 8 agreeing frames. At frame 16 one WAIT withdraws SAFE on the same frame.

## Slide 19
WORKFLOW
Three states, one default
Safe Road-Crossing Assistance System · Review Round 1
19
SEARCHING
no confident crosswalk
WAITING
the default
SAFE TO CROSS
earned, never assumed
crosswalk found
8-frame vote
crosswalk lost
8-frame vote
green + clear road
8 consecutive frames
any danger
next frame, no vote
crosswalk lost while SAFE: immediate, no vote
start
Every transition needs an 8-frame vote, with one exception: leaving SAFE is instant. Only SAFE TO CROSS ever produces a “safe to cross” announcement.
Notes: The rules only ever emit three states. Transitions into any state are debounced by an 8-frame vote; the single exception is leaving SAFE_TO_CROSS, which happens on the next disagreeing frame. WAITING is drawn largest because it is the default.

## Slide 20
WORKFLOW
Project workflow: from data to decisions you can audit
Safe Road-Crossing Assistance System · Review Round 1
20
01
Collect
public datasets + own crossing footage
02
Unify
remap every source to the same 10 classes
03
Label
model-assisted pre-labels, human-checked
04
Train
YOLOv8 detector, 960 px input
05
Integrate
one phase at a time, each run end-to-end
06
Log
every decision to SQLite
PLANNED EVALUATION · LATER ROUNDS
Replay recorded crossings, compare every logged decision with hand-annotated ground truth, and score the two kinds of error separately, never averaged together.
False-SAFE rate
primary metric: SAFE said while the road was dangerous
False-WAIT rate
secondary: the usability cost of caution
Withdraw latency
frames from danger appearing to WAIT
Throughput
frames per second on a CPU
Notes: Build workflow: collect, unify classes, label, train, integrate phase by phase, log. Evaluation is planned for later rounds: decision logs are compared frame-by-frame with hand-annotated ground truth, and false-SAFE and false-WAIT are reported separately because their costs are not comparable. No whole-system accuracy is claimed yet.